## Slide 1: Internship Oral Presentation
By: Tay Kong Chun, Victor
Temasek Laboratories

## Slide 2: Contents
Objectives for this Internship
What had been achieved?
What is Visual Odometry?
What is SLAM?
Pros and Cons
VIO: S-MSCKF
SLAM: ORB_SLAM2
Improved Implementation Design
Future Works
What have I learnt from this Internship?

## Slide 3: Objectives for this Internship
To assist the Control and Guidance Group in developing and improving on an existing visual odometry system for Unmanned Aerial Vehicle.
  Fully understand the workings of the current visual odometry system used
  Design and improve on the current visual odometry system used
    Adding loop-closure algorithm to enhance the system to be more robust and accurate
    Proper documentation of the design
    Implement the improved designed visual odometry system

## Slide 4: What had been achieved?
Fully broken down the current visual odometry system used
Designed the addition of loop-closure algorithm from another well tested system to enhance the current system
Prepared proper documentation of the design
Implemented most of the improved designed visual odometry system

## Slide 5: What is Visual Odometry (VO)?
Estimating the motion of a camera in real time using sequential images
Usually done with either Mono or Stereo camera setup
Used when GPS is unable to provide a position estimation of camera in real time
Can be further enhanced with the use if Inertia-Measurement Unit (IMU) for added robustness and accuracy
  System is called Visual Inertia Odometry (VIO)

## Slide 6: What is Visual Odometry (VO)?

## Slide 7: What is SLAM?
Simultaneous Localization and Mapping (SLAM)
Estimating the motion of a camera in real time using a map
Map of an unknown environment is drawn using feature points detected in the images captured by the camera
All are done concurrently
Usually done with either Mono or Stereo camera setup
Used when GPS is unable to provide a position estimation of camera in real time
Can be further enhanced with the use if Inertia-Measurement Unit (IMU) for added robustness and accuracy

## Slide 8: What is SLAM?
Position Estimation Drift Error

## Slide 9: Pros and Cons
Visual Inertia Odometry (VIO)
Pros
  Faster algorithm frequency
  Lesser computational requirement
Cons
  Less accurate robust
  Very susceptible to drift over time
Simultaneous Localization and Mapping (SLAM)
Pros
  More accurate and robust
  Able to detect past frames and correct drift
Cons
  Slower algorithm frequency
  Higher computational requirement

## Slide 10: VIO: S-MSCKF
Current system used by Control and Guidance Group
Stereo RGB Camera setup
Semi-direct method
Fast algorithm frequency
Requires only a small sensor package
Stereo Camera and IMU
More accurate and more efficient than state-of-art monocular solutions
Compared to VINS-Mono and OKVIS

## Slide 11: VIO: S-MSCKF
Difference between EKF SLAM, keyframe-based SLAM and MSCKF
Semi-direct method using optical flow

## Slide 12: SLAM: ORB_SLAM2
State-of-art SLAM algorithm
Capable of using multiple types of camera setup
Mono, Stereo, RGB-D
Feature-based method
Relatively slow algorithm frequency
Requires only a small sensor package
Mono, Stereo or RGB-D camera
Robust and accurate loop-closure algorithm to correct drift-error in position estimation over time

## Slide 13: SLAM: ORB_SLAM2
Example of loop detected
Loop detection and fusion with backward correction

## Slide 14: SLAM: ORB_SLAM2
Loop detection with severe scale change and dynamic objects in the image
Collections of keyframes with feature points in a map

## Slide 15: Improved Implementation Design
Big difficulty in porting the loop-closure algorithm only from ORB_SLAM2 to S-MSCKF
ORB_SLAM2 is Feature-based while S-MSCKF is Semi-direct Optical Flow
Proposed design:
Use S-MSCKF as the main Tracking algorithm to replace the Tracking algorithm thread in ORB_SLAM2
Pass the finalized corrected pose to S-MSCKF for pose correction after loop fusion in ORB_SLAM2
Reset Sliding Window in S-MSCKF after pose correction

## Slide 16: New Implementation Design
S-MSCKF
Loop_Closure
New Camera Image
Pose Estimation of Current Frame
ORB_SLAM2
Create New Keyframe
Detect Loop
Corrected Pose of Current Frame
Send Corrected Pose
Replace Pose with Corrected Pose
Send Corrected Pose
Reset Sliding Window

## Slide 17: New Implementation Design
Implementation:
Everything is coded with the new implementation design
Current Issues:
Multi-thread randomly kill the node
Very computationally heavy
Overall algorithm frequency is low
Code is not optimised

## Slide 18: Future Works
Fix the issue of multi-thread randomly kill the node
Find ways to optimise the code

## Slide 19: What have I learnt from this Internship?
Self learning is very important
Must keep a detailed documentation of everything that is done
Must be able to communicate ideas and information clearly with others
Thinking out of the box for solution is key to solving problems

## Slide 20: Thank You!
Any Questions?